Section 1 - Chemical Product and Company Identification

Product/Chemical Name:  Alumina Trihydrate

Synonyms: Alumina Hydrate, ATH, Aluminum Hydroxide, Trihydrate D’aluminae, Hydrate d’aluminae, Gibbsite, Hydroxide d’aluminum, Alumine hydrate, hydrated alumina, Trioxyde d’aluminum, Aluminum Trihydroxide, Al203·3H2O

General Use: refractory material, abrasive, fire retardant and smoke suppressant for plastics, ceramic material.

Manufacturer:  The R. J. Marshall Company			Emergency Phone:  (800) 424-9300

26776 W. 12 Mile Road				Date Revised:  5/29/13

Southfield, MI  48034-7807			Preparer: Stephanie Nichols

Phone (248) 353-4100, Fax (248) 948-6460

Section 2 - Hazards Identification

| HMIS |
| --- |
| H F R | 1 0 0 |
| PPE† E †Sec. 8 |

(((((  Emergency Overview (((((

Potential Health Effects

Warning:  Irritant, R37

Primary Entry Routes:  Inhalation

Acute Effects

Inhalation: Inhalation of high concentrations of this inert nuisance particulate can result in mild irritation of the respiratory tract.

Eye: May cause irritation through mechanical abrasion.

Skin: May cause irritation through mechanical abrasion.

Ingestion: Unlikely.

Medical Conditions Aggravated by Long-Term Exposure: n/a

Section 3 - Composition / Information on Ingredients

| Ingredient Name | CAS Number | Weight |
| --- | --- | --- |
| Alumina Trihydrate | 21645-51-2 | 100% |

Section 4 - First Aid Measures

Inhalation: If overcome by high dust concentrations, remove to a ventilated area.

Eye Contact:  Flush eyes thoroughly for 15 minutes taking care to rinse under eyelids.  Do not scrub.  Abrasion may cause irritation.  If discomfort continues, continue to wash with water.  If irritation persists, consult a physician.

Skin Contact: Wash skin thoroughly with soap and water for at least 15 minutes.  Consult a physician if irritation persists.

Ingestion: If swallowed, dilute with large amounts of water.  Do not induce vomiting.  Consult a physician immediately.

After first aid, get appropriate in-plant, paramedic, or community medical support.

Note to Physicians: n/a

Special Precautions/Procedures: n/a

Section 5 - Fire-Fighting Measures

Flash Point: None known.

Flash Point Method: n/a

Burning Rate: Does not burn.

Auto-ignition Temperature: Does not ignite.

Flammability Classification: n/a

Extinguishing Media: Water spray, carbon dioxide, or other dry chemical.

Unusual Fire or Explosion Hazards: None known.

Hazardous Combustion Products: None.

Fire-Fighting Instructions: Do not release runoff from fire control methods to sewers or waterways.

Fire-Fighting Equipment: Because fire may produce toxic thermal decomposition products, wear a self-contained breathing apparatus (SCBA) with a full face-piece operated in pressure-demand or positive-pressure mode.

Section 6 - Accidental Release Measures

Spill /Leak Procedures: Collect solids.  Recycle if possible.

Regulatory Requirements: Follow applicable OSHA regulations (29 CFR 1910.120).

Section 7 - Handling and Storage

Handling Precautions: Avoid generating dust during handling.

Storage Requirements: Keep material dry.

S-phrases:  S8, S36/37/39

Section 8 - Exposure Controls / Personal Protection

|  | OSHA PEL | ACGIH TLV |
| --- | --- | --- |
| Ingredient | TWA | STEL | TWA | STEL |
| Alumina Trihydrate | none estab. | none estab. | none estab. | none estab. |
| Nuisance Dust | 15 mg/m3 total, 5 mg/m3 respirable | none estab. | none estab. | none estab. |

Engineering Controls:

Ventilation: Provide general or local exhaust ventilation systems to maintain airborne concentrations below OSHA PELs (Sec. 2). Local exhaust ventilation is preferred because it prevents contaminant dispersion into the work area by controlling it at its source.

Administrative Controls:

Protective Clothing/Equipment: Wear tightly fitting safety goggles or safety glasses with side shields.

Contaminated Equipment: Separate contaminated work clothes from street clothes. Launder before reuse. Remove this material from your shoes and clean personal protective equipment.

Comments: Never eat, drink, or smoke in work areas. Practice good personal hygiene after using this material, especially before eating, drinking, smoking, using the toilet, or applying cosmetics.

Section 9 - Physical and Chemical Properties

| Physical State: white powder Appearance and Odor: white odorless powder Odor Threshold: n/e Vapor Pressure: n/e Vapor Density (Air=1): n/a Formula Weight: n/a Density: 8-80lb/ft3 Specific Gravity (H2O=1, at 4 °C): 2.4 pH: 8.5-10.2 (20% solution) | Water Solubility: Insoluble Other Solubilities: Soluble in alkaline aqueous solutions or in HCL, H2SO4, and other strong acids in the presence of some water. Boiling Point: n/a Melting Point: 3700F (2038C) Viscosity: n/a Refractive Index: n/a Surface Tension: n/a % Volatile: n/a Evaporation Rate: n/a |
| --- | --- |

Section 10 - Stability and Reactivity

Stability: Alumina trihydrate is stable at room temperature in closed containers under normal storage and handling conditions.

Polymerization: Hazardous polymerization cannot occur.

Chemical Incompatibilities: Strong acids and bases.  Alumina trihydrate reacts vigorously with strong acids and will dissolve in caustic solutions.

Reactivity with Heat: When exposed to fire or heat, hydrated alumina loses its water of crystallization beginning at 392F (200C).

Hazardous Decomposition Products: n/a

Section 11- Toxicological Information

Toxicity Data:*

| Eye Effects: Nuisance dust. May cause irritation through mechanical abrasion. Flush with water for at least 15 minutes. Consult physician if irritation is persistent. Skin Effects: Nuisance dust. May cause irritation through mechanical abrasion. Wash skin thoroughly with soap and water. | Acute Inhalation Effects: Nuisance dust. Overexposure to dust may cause irritation to the respiratory tract. Should this occur, remove affected individual to fresh air. If symptoms persist, consult a physician. Acute Oral Effects: None known. Chronic Effects: None known. Carcinogenicity: Neither this product nor any of its components are considered carcinogenic by OSHA, IARC, NTP, or ACGIH. |
| --- | --- |

Section 12 - Ecological Information

No information available.

Section 13 - Disposal Considerations

Disposal: Recycle if possible or landfill.  This substance is inert and does not require special disposal methods.  Follow applicable Federal, state, and local regulations.

Section 14 - Transport Information

DOT Transportation Data (49 CFR 172.101):  This product is not classified as dangerous under the transport regulations for road, rail, sea, or air transport.

Section 15 - Regulatory Information

EPA Regulations:

RCRA Hazardous Waste Number: Not listed (40 CFR 261.33)

RCRA Hazardous Waste Classification (40 CFR 261.??): Not classified

CERCLA Hazardous Substance (40 CFR 302.4) not listed

SARA Toxic Chemical (40 CFR 372.65): Not listed

SARA EHS (Extremely Hazardous Substance) (40 CFR 355): Not listed

OSHA Regulations:

Air Contaminant (29 CFR 1910.1000, Table Z-1, Z-1-A): Not listed

OSHA Specifically Regulated Substance (29CFR 1910.????)

Inventory Lists:  This product is listed on the following inventory lists:

| TSCA | Australia AICS | Canada DSL | China IECSC | Europe EINECS | Japan ENCS | Korea ECL |
| --- | --- | --- | --- | --- | --- | --- |
| Listed | Listed | Listed | Listed | 244-492-7 | 1-17 | KE-00980 |

| New Zealand NZIoC | Swiss Giftliste | Philippines PICCS | Taiwan NECI |
| --- | --- | --- | --- |
| Listed | G-4621 | Listed | Listed |

Section 16 - Other Information

Prepared By: Stephanie Nichols

Revision Notes: Added MX104

Product Grades Available from the R. J. Marshall Company (this list may be incomplete):

| DF40 | OFI | A202 (A,W) | AH170(A,C,V) | DGXW1 |
| --- | --- | --- | --- | --- |
| DF45 | OFIII | A203H | AH190 | DGXW2 |
| DF74 | OFV | A204(A,W) | AH255(A,W) | EM107 |
| DF80 | OFVS | A205(A) | AH270(A,C,V, W) | EXT DF 168 |
| DF80S | OFVI | A206(A,H,W) | AH280(A,C,V,W) | ATH-A |
| DF85 | OF7 | A208(A) | AH285W | ATH-B |
| DF111 | OF136 | A210(A) | AH290(A,C,V,W) | DT1080 |
| DF119 | OF250 | A210SP | AH290S | KX-1 |
| DF121 | OF255A | A212(A) | AH298(A,C) | DT1186 |
| DF132 | OF300 | A245(W) | AH330(A,C,V,W) | STM1410 |
| DF161 | OF500 | A236HL | AH331(A) | AC470AN |
| DF174 | OF505 | A200SB1 | AH430(A,C,H,V,W) | AC480AN |
| DF211(A) | OF600 | RC802(A) | AH610 |  |
| DF221 |  |  | AH690 |  |
| DF225 | OR150 | A102 | AH171(A) |  |
| DF230 | OR250 | A104 | AH271(A) |  |
| DF240 | OR255A | A105 | AH281(A) |  |
| DF270 | RC822 | A106 | AH291(A) |  |
| DF315 | A4555 | A108 | AH331(A) |  |
| DF320A | 8515 | A110 | AH431(A) |  |
| DF325(C,W) | HF136 | A112 | AH691 |  |
| DF420 |  | A130 | AF330(A) |  |
| DF1045 | MX100 | A145 |  |  |
| DF1051 | MX104 | A104A |  |  |
| DF2040 | MX200 |  |  |  |
| DFG |  |  |  |  |

Note:  This includes all EXP ATH blends.

Disclaimer: Information contained herein is presented in good faith and is based on data believed to be accurate.  However no warranty is expressed or implied regarding this information or the results obtained from the use of this Material Safety Data Sheet, whether it originates with The R. J. Marshall Company or others.  This Safety Data Sheet relates only to the specific material designated herein.  It does not relate to use with other material or processes.  This information is supplied with the condition that the user will make appropriate determination as to its suitability for their purpose prior to using it.